## Slide 1: SMART INDIA HACKATHON 2026
Problem Statement ID – 26011
Problem Statement Title – 3D ULPIN Generation and Vertical Property Mapping System
Theme – Space Technology
PS Category – Software
Team ID – SIH_1184 GeoGraph
Team Name – GeoGraph

## Slide 2
GeoGraph
The gap: ULPIN identifies land, while buildings occupy volume
A 2D parcel identifier cannot distinguish legally different spaces stacked over the same footprint.
SMART INDIA HACKATHON 2026 | TEAM GEOGRAPH
02
CURRENT LIMITATION
One surface parcel, many claims
• The existing ULPIN is a strong root identity for the surface parcel.
• Flats, basements, podiums, tunnels and air rights can share the same 2D footprint.
• A deed or plan may describe height and use, but the parcel ID does not encode them.
• Overlap is discovered late, during registration, financing or dispute resolution.
Problem signal
Same ground footprint does not mean same property volume.
PROPOSED MODEL
Root ULPIN + volumetric child IDs
Each register entry combines footprint, elevation range, use class, tenure and right holder.
AIR RIGHTS / TDR
above +32.0 m
FLAT 402
26.9 m to 30.1 m
FLAT 302
23.7 m to 26.9 m · 3D ULPIN issued
PODIUM + COMMERCIAL
4.5 m to 23.7 m
SURFACE PARCEL
root ULPIN at 0.0 m
BASEMENT PARKING B1
−3.2 m to 0.0 m
METRO / UTILITY CORRIDOR
below −18.0 m
Design outcome · a conflict becomes a geometry check before registration
Notes: Conceptual basis: existing 14-character ULPIN remains the root identity. Proposed child identifiers add a volume marker, base/top elevation, use class and tenure. Reference models: DoLR ULPIN/Bhu-Aadhaar, ISO 19152 LADM Part 2 and OGC CityGML 3.0.

## Slide 3
GeoGraph
One data model powers the map, 3D view and registry
The proof-of-concept uses a live spatial pipeline with an identifier that can be validated offline.
SMART INDIA HACKATHON 2026 | TEAM GEOGRAPH
03
TECHNOLOGY STACK
Web + UI
TypeScript · React · Vite
Design system
Tailwind CSS · responsive surfaces
Map + 3D
MapLibre GL · Three.js / deck.gl
Spatial rules
PostGIS · Turf.js · topology checks
Backend
Node/Fastify API · WebSocket/SSE
ID codec
Rust codec · deterministic parsing
REFERENCE ARCHITECTURE
01 INPUT SOURCES
• GIS parcel layers
• CORS / GNSS fixes
• DEM / DSM and imagery
• Approved floor plans
02 SPATIAL ENGINE
• Footprint alignment
• Floor-plan digitisation
• Elevation-range tests
• Tolerance and topology
03 3D ULPIN CODEC
• Root parcel ULPIN
• Volume marker
• Base / top elevation
• Use class + tenure
04 REGISTRY + CLIENTS
• PostgreSQL / PostGIS register
• Live map + 3D scene
• Offline validator
• GeoJSON · CityGML · LADM
One scene state keeps the cadastral map and the 3D volume view consistent.
Notes: Technology choices from the source deck: TypeScript, React, Vite, Tailwind, MapLibre GL, Three.js/deck.gl, PostGIS, Turf.js, Node/Fastify, Rust ID codec, WebSocket/SSE, GeoJSON, CityGML 3.0 and LADM.

## Slide 4
GeoGraph
From survey to registry: a six-step issuance loop
The workflow converts ordinary survey and planning records into validated volumetric register entries.
SMART INDIA HACKATHON 2026 | TEAM GEOGRAPH
04
IMPLEMENTATION FLOW
01
Ingest
CORS/GNSS
imagery + DEM/DSM
02
Survey
Fix footprint
bind root ULPIN
03
Digitise
Trace floor plan
into storeys
04
Extrude
Footprint +
elevation range
05
Issue
Mint 3D ULPIN
per volume
06
Validate
Overlap check
write registry
IDENTIFIER ANATOMY
The string carries the parcel, volume and vertical extent without a database lookup.
RJ09JPR0A1B2C3
root parcel ULPIN
V
volume marker
+02370
base elevation (cm)
+02690
top elevation (cm)
R
use class + tenure
Validation rule: same footprint + intersecting elevation range = review flag before registration.
Notes: Process from source deck: ingest CORS/GNSS, imagery, DEM/DSM and GIS parcels; survey the footprint and bind the root ULPIN; digitise floor plans; extrude volumes; issue an ID; validate overlap and write to an append-only registry.

## Slide 5
GeoGraph
Feasibility: high leverage, bounded hackathon scope
The MVP can prove the core idea with one ward, one dataset and three user-facing surfaces.
SMART INDIA HACKATHON 2026 | TEAM GEOGRAPH
05
DELIVERY CASE
BUILDABLE NOW
• Existing ULPIN remains untouched.
• Survey of India CORS/GNSS provides the positioning base.
• Inputs already exist: GIS parcels, floor plans, DEM/DSM and imagery.
• Thin vertical slice fits a hackathon build.
KEY RISKS
• Local floor levels may use different vertical datums.
• Scanned plans may be rotated or not georeferenced.
• State DCRs define use, tenure, air rights and TDR rules.
• Survey noise can create false overlap signals.
MVP CONTROLS
• Store one geoid-referenced datum plus source metadata.
• Use assisted digitisation with a human review step.
• Make tenure and use class pluggable by state.
• Apply tolerance bands and append-only versioning.
ADOPTION PATH
01
WARD PILOT
One ULB ward
three surfaces
02
DISTRICT
More parcels
shared standards
03
STATE
DCR vocabulary
registry integration
04
INTEROPERABILITY
LADM / CityGML
exchange layer
Adoption principle: add vertical child records without re-issuing the existing root ULPIN.
Notes: Feasibility and risk framing from the source deck: extend the existing ULPIN layer; use CORS/GNSS, floor plans, drone/LiDAR tiles, DEM/DSM and GIS parcel layers; normalize vertical datum, assist digitisation, use state-pluggable DCR fields, apply tolerance bands and write append-only versions.

## Slide 6
GeoGraph
Impact and reference base
The value compounds when ownership, geometry and verification share one record.
SMART INDIA HACKATHON 2026 | TEAM GEOGRAPH
06
WHY IT MATTERS
26
States & UTs already on ULPIN
±3 cm
CORS / RTK positioning cited in the source deck
OFFLINE
ID validation without a registry lookup
A parcel record that names the volume you bought, financed or regulated.
CITIZENS, HOUSING SOCIETIES AND ULBS
• Flats, parking, basements and common areas get explicit volumetric records.
• Boundary disputes become checkable geometry instead of competing descriptions.
• A shared identifier gives owners, tenants and local bodies the same reference.
BANKS, INSURERS AND GOVERNANCE
• Air rights and TDR gain a register entry that can be audited.
• Double-mortgaging the same cubic metres becomes a geometry query.
• FSI, height, daylight and underground utility checks get a spatial record.
REFERENCE BASE
DoLR ULPIN / Bhu-Aadhaar · Survey of India CORS · SIH PS 26011 · ISO 19152-1 / 2 · OGC CityGML 3.0
Notes: References from the source deck: dolr.gov.in; surveyofindia.gov.in; sih.gov.in; iso.org/standard/81263.html; iso.org/standard/81264.html; ogc.org/standard/citygml. The metric labels preserve the source deck's cited context and should be rechecked against the latest official publications before final submission.